## Slide 1: Experience: Large-scale Cellular Localization for Pickup Position Recommendation at Black-hole
Shuli Zhu1, Lingkun Li1, Xuyu Wang2, Changcheng Liu3, Yuqin Jiang3, Zengwei Huo3,
Hua Chai3, Jiqiang Liu1, Dan Tao1, Ruipeng Gao1*
1Beijing Jiaotong University
2Florida International University
3DiDi
*Corresponding Author
ACM MobiCom 2023
Madrid, Spain

## Slide 2: Motivation
Accurate pickup service
  Ride-hailing platforms, like DiDi, Uber, and Lyft
  Pickup location
    Connection between drivers and passengers utilizing passengers’ location
Why cellular? Why not GPS or Wi-Fi?
  A remarkable observation in DiDi platform
    Over 68,000 daily travel orders (~2% of the total) originate from locations with no GPS signals or no pre-collected Wi-Fi fingerprint data
Black-hole
  Passengers rely solely on cellular localization
    No GPS signals, no pre-collected WiFi fingerprint data, and no dedicated hardware deployment
    e.g., subway stations, underground parking structures, and large shopping malls

## Slide 3: Challenge
Accurate and scalable cellular localization for pickup service
at a large scale in the industry

## Slide 4: Cell Tower Measurements
User Measurement Data in LTE/NR networks from smartphones
  Serving tower details (take 4G LTE as an example)
    Mobile Country Code (MCC)
    Mobile Network Code (MNC)
    Tracking Area Code (TAC)
    Cell ID (CID)
    E-UTRA Absolute Radio Frequency Channel Number (EARFCN)
    Physical Cell Identifier (PCI)
    Reference Signal Received Power (RSRP)
    Reference Signal Received Quality (RSRQ)
  Neighboring towers
    Only EARFCN, PCI, RSRP, and RSRQ

## Slide 5: Cell Tower Augmentation
Challenges in cellular localization
  Sparse cell towers
 | 1 Tower | 2 Towers | 3 Towers | >3 Towers
4G LTE | 44.82% | 4.83% | 7.68% | 42.67%
5G NR | 53.48% | 2.68% | 5.50% | 38.34%
Urban area of 4 km2, Beijing

## Slide 6: Cell Tower Augmentation
Challenges in cellular localization
  Sparse cell towers
  Unbalanced user fingerprints

## Slide 7: Cell Tower Augmentation
Challenges in cellular localization
  Sparse cell towers
  Unbalanced user fingerprints
  Temporal variations

## Slide 8: Cell Tower Augmentation
Augmented cell towers as a primitive
  PCI & EARFCN
    They are present in both serving tower and neighboring towers
  We adopt the pair (PCI, EARFCN) as the unique index for “augmented” towers
    With augmentation, the number of augmented towers are twice than the amount of primary towers

## Slide 9: System Overview
Fingerprint Set Construction
Real Time Localization
Receptive region
User popularity
Cellular signature
Candidate region
CNN
Outdoor
Black-hole
Feature map
Pickup Recommendation
Pickup position
Candidates
DeepFM model

## Slide 10: Fingerprint Set Construction
Data collection process
  Outdoor trajectories
    Geo-tag (accurate GPS location) with associated cellular information
We do NOT use INDOOR trajectories

## Slide 11: Fingerprint Set Construction
Four-step construction process
  Map grid partitioning
  Receptive region production

## Slide 12: Fingerprint Set Construction
Four-step construction process
  Map grid partitioning
  Receptive region production
  Cellular signature representation
    Bucket-based Storing Mechanism not Gaussian distribution
    We store cellular signatures as an INT64 integer for each grid cell

## Slide 13: Fingerprint Set Construction
Four-step construction process
  Map grid partitioning
  Receptive region production
  Cellular signature representation
  User popularity counting
    Page View (PV)
      The total number of samples collected at a grid cell over some time ,
    Unique Visitor (UV)
      The number of associated user collecting the samples at this grid over the period,
    With a Gaussian time decay factor
      Recent visits are more valuable
      The duration is a month in our system

## Slide 14: Real Time Localization
Candidate region production
Feature map generation
  RSRP signature similarity
  RSRQ signature similarity
  PV heat feature
  UV heat feature
CNN model for localization
  Structure
    3 convolutional layers
    2 fully connected layers
  Loss
    We calculate great-circle distance between predicted location and its ground truth (geo-tag)

## Slide 15: Pickup Recommendation
Road discretization
Candidate estimation
Customized recommendation
  Stage 1: Pairwise ranking instead of binary classification
  Stage 2: Deep neural model
Pickup position
Candidates
DeepFM model

## Slide 16: Evaluation: Data Set Collection
Past 2 years
~50M orders, ~13M devices
  918 brands, and ~9300 models of smartphones
4541 cities in China
Only focusing on Android platform
  iOS provides its built-in cellular localization service

## Slide 17: Evaluation Metrics
Pickup position error
  The distance between recommended and actual pickup positions
Over-30-meters ratio
  The ratio of the pickup position error higher than 30 meters
Cancel ratio
  The passengers cancel the order
Call ratio / Long call ratio
  Call between passengers and drivers
    Long call means the duration exceeds 60s
Pickup Position Error | 0~30m | 30~50m | 50~100m | >100m
Call Ratio | 17.76% | 33.28% | 48.28% | 69.87%
Long Call Ratio | 0.74% | 4.30% | 10.61% | 27.08%

## Slide 18: Overall Performance
Compared with iOS
  iOS advantages (Our)
    System-level privilege (Application-level)
    Homogeneous environment ( Numerous manufacturers)
Compared with alternatives
  DCCP, DeepLoc
  NBL, GMM, CID
Compared with DMM
  Precision increased by 9.43%
  Recall increased by 8.41%

## Slide 19: Evaluation Details (1/4)
Performance across different scale of cities
Performance among 12 months at three typical cities

## Slide 20: Evaluation Details (2/4)
Performance of different phone brands and models

## Slide 21: Evaluation Details (3/4)
Performance across different service providers
Comparison between 4G LTE and 5G NR
  4G LTE network with different fingerprint density

## Slide 22: Evaluation Details (4/4)
Effect of localization hyper-parameters
CNN features and recommendation stage comparison

## Slide 23: Conclusion
Summary
  Practical Deployment and Evaluation
    A dataset of 50 million travel orders across 13 million devices, spanning 4,541 cities
  Novel Crowdsensing Approach
    No need for labor-intensive indoor fingerprint collection
  New Service Metrics for Large-scale Evaluation
    Pickup position error, over-30-meters ratio, cancel ratio, and call ratio
Future work
  Abnormal cell towers detection
    Anomaly detection by Generative Adversarial Networks (GAN)

## Slide 24
Thanks!
Q & A